## Slide 1: DEFINITION OF SOIL
  Soil is a natural body:
  solids (minerals and organic matter),
  liquid,
  and gases
  Soil is formed over a long period of time. It can take 1000 years or more. Soil is formed from the weathering of rocks and minerals. The surface rocks break down into smaller pieces through a process of weathering and is then mixed with moss and organic matter.

## Slide 2: SOIL FORMATION
Weathering is the process of the breaking down rocks:
Physical weathering: it breaks down the rocks, but what it's made of stays the same.
Chemical weathering it still breaks down the rocks, but it may change what it's made of. For instance, a hard material may change to a soft material after chemical weathering.

## Slide 3: SOIL PROFILE

## Slide 4: SOIL TYPES
SOIL TYPES
  RESIDUAL SOIL
  SEDIMENT SOIL
    ALLUVIUM SOIL
    LACUSTRINE SOIL
    MARINE SOIL
  PARTICULAR SOIL (Problematic Soils)
    EXPANSIVE SOIL
    ORGANIC SOIL
    COLLAPSIBLE SOIL
    QUICK CLAY
    LIQUEFIABLE SOILS

## Slide 5
PARTICLE BONDING
    THE PARTICLE BONDING IS VERY WEAK SO RELATIVELY EASY TO GOING TO CHANGE AND HAVE NON-LINEAR BEHAVIOUR AND CHARACTERISTIC
SHAPE, SIZE AND STRUCTURE OF SOIL PARTICLE
Cohesive Soil
Non-cohesive Soil
BASIC CHARACTERISTIC

## Slide 7
LOOSE SAND
DENSE SAND

## Slide 8: 1. Soil Formations and Deposits

## Slide 9: 1.1 Rock Cycles
Soils
(Das, 1998)
The final products due to weathering are soils

## Slide 10: Question What is the main mineral of the sand particles in general?
Quartz
Notes: Calcareous sand

## Slide 11: 1.3 Weathering
1.3.1 Physical processes of weathering
  Unloading
    e.g. uplift, erosion, or change in fluid pressure.
  Thermal expansion and contraction
  Alternate wetting and drying
  Crystal growth, including frost action
  Organic activity
    e.g. the growth of plant roots.
1.3.2 Chemical Process of weathering
  Hydrolysis
    is the reaction with water
    will not continue in the static water.
    involves solubility of silica and alumina
  Chelation
    Involves the complexing and removal of metal ions .
  Cation exchange
    is important to the formation of clay minerals
  Oxidation and reduction.
  Carbonation
    is the combination of carbonate ions such as the reaction with CO2
1.3.3 Factors affect weathering
  Many factors can affect the weathering process such as climate, topography, features of parent rocks, biological reactions, and others.
  Climate determines the amount of water and the temperature.
(Mitchell, 1993)

## Slide 12: 1.4 Transportation of Weathering Products
1.4.1 Residual soils-
to remain at the original place
  In some areas, the top layer of rock is decomposed into residual soils due to the warm climate and abundant rainfall .
  Engineering properties of residual soils are different with those of transported soils
  The knowledge of "classical" geotechnical engineering is mostly based on behavior of transported soils. The understanding of residual soils is insufficient in general.
1.4.2 Transported soils-
to be moved and deposited to other places.
  The particle sizes of transported soils are selected by the transportation agents such as streams, wind, etc.
    Interstratification of silts and clays.
  The transported soils can be categorized based on the mode of transportation and deposition (six types).

## Slide 13
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Mechanical erosion due to ocean waves and wind at Yehliu, Taiwan

## Slide 14
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Mechanical erosion due to ocean waves and wind at Yehliu, Taiwan

## Slide 15
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Mechanical erosion due to ocean waves and wind at Yehliu, Taiwan

## Slide 16
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Mechanical erosion due to ocean waves and wind at Yehliu, Taiwan

## Slide 17
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Mechanical erosion due to ocean waves and wind at Yehliu, Taiwan

## Slide 18: 1.4.2 Transported Soils (Cont.)
(1) Glacial soils: formed by transportation and deposition of glaciers.
(2) Alluvial soils: transported by running water and deposited along streams.
(3) Lacustrine soils: formed by deposition in quiet lakes.
(4) Marine soils: formed by deposition in the seas.
(5) Aeolian soils: transported and deposited by the wind.
(6) Colluvial soils: formed by movement of soil from its original place by gravity, such as during landslide. (from Das, 1998)

## Slide 19: 2.1 Karsts and Caverns
Calcium carbonate can dissolve in water through the following reaction and form the so-called Karst topography.
CO2+H2O+CaCO3Ca2++2HCO3-
The underground hollows (caverns) are troublesome to the foundation design.

## Slide 20: 2.4 Colluvial soils
Colluvial soils
  The colluvial soils mainly originate from the landslide and they are usually poorly consolidated.
Colluvial soils
Slope
Notes: About 15 % of the land area of the Territory is covered with colluvium. Colluvium generally accumulates at footslopes or in gullies at upper levels. However, thin veneers of colluvial deposit are noted on side slopes. These colluvial deposits have resulted from the mass movements in the geological past and is usually poorly consolidated.

## Slide 21: IV Clay Minerals and Soil Structure

## Slide 22: 1. Clay Minerals

## Slide 23: Outline
Clay Minerals
Identification of Clay Minerals
Specific Surface (Ss)
Interaction of Water and Clay Minerals
Interaction of Clay Particles
Soil Structure and Fabric
Soil Fabric-Natural Soil
Soil Fabric-Clay Soils
Soil Fabrics-Granular Soils
Loess
Suggested Homework
References

## Slide 24: 1.1 Origin of Clay Minerals
“The contact of rocks and water produces clays, either at or near the surface of the earth” (from Velde, 1995).
Rock +Water  Clay
For example,
The CO2 gas can dissolve in water and form carbonic acid, which will become hydrogen ions H+ and bicarbonate ions, and make water slightly acidic.
CO2+H2O  H2CO3 H+ +HCO3-
The acidic water will react with the rock surfaces and tend to dissolve the K ion and silica from the feldspar. Finally, the feldspar is transformed into kaolinite.
Feldspar + hydrogen ions+water  clay (kaolinite) + cations, dissolved silica
2KAlSi3O8+2H+ +H2O  Al2Si2O5(OH)4 + 2K+ +4SiO2
Note that the hydrogen ion displaces the cations.
Notes: Steady water cannot sustain the reaction.

## Slide 25: 1.1 Origin of Clay Minerals (Cont.)
The alternation of feldspar into kaolinite is very common in the decomposed granite.
The clay minerals are common in the filling materials of joints and faults (fault gouge, seam) in the rock mass.
Weak plane!

## Slide 26: 1.2 Basic Unit-Silica Tetrahedra
Hexagonal
hole
1 Si
4 O
(Si2O10)-4
Replace four Oxygen with hydroxyls or combine with positive union
(Holtz and Kovacs, 1981)
Tetrahedron
Plural: Tetrahedra

## Slide 27: 1.2 Basic Unit-Octahedral Sheet
Gibbsite sheet: Al3+
Al2(OH)6, 2/3 cationic spaces are filled
One OH is surrounded by 2 Al: Dioctahedral sheet
Brucite sheet: Mg2+
Mg3(OH)6, all cationic spaces are filled
One OH is surrounded by 3 Mg: Trioctahedral sheet
Different cations
1 Cation
6 O or OH
(Holtz and Kovacs, 1981)

## Slide 28
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
(a) Silica tetrahedron; (b) silica sheet; (c) alumina octahedron; (d) octahedral (gibbsite) sheet; (e) elemental silica-gibbsite sheet; (after Grim, 1959)

## Slide 29: 1.2 Basic Unit-Summary
Mitchell, 1993

## Slide 30: 1.3 Synthesis
Noncrystalline clay -allophane
Mitchell, 1993
Notes: Copy the table to students (Table 3-3, Mitchell’s book)
I will only introduce common clay minerals which are quite often encountered by engineers.
The bonding between the sheet is convalent bond.

## Slide 31: 1.4 1:1 Minerals-Kaolinite
Basal spacing is 7.2 Å
Si4Al4O10(OH)8. Platy shape
The bonding between layers are van der Waals forces and hydrogen bonds (strong bonding).
There is no interlayer swelling
layer
Trovey, 1971 ( from Mitchell, 1993)
17 m
Notes: Mineral particles of the kaolinite subgroup consists of the basic units stacked in the c direction. The bonding between successive layers is by both van der Waals forces and hydrogen bonds. The bonding is suffi

## Slide 32: 1.4 1:1 Minerals-Halloysite
Si4Al4O10(OH)8·4H2O
A single layer of water between unit layers.
The basal spacing is 10.1 Å for hydrated halloysite and 7.2 Å for dehydrated halloysite.
If the temperature is over 50 °C or the relative humidity is lower than 50%, the hydrated halloysite will lose its interlayer water (Irfan, 1966). Note that this process is irreversible and will affect the results of soil classifications (GSD and Atterberg limits) and compaction tests.
There is no interlayer swelling.
Tubular shape while it is hydrated.
Trovey, 1971 ( from Mitchell, 1993)
2 m
Notes: Classification and compaction tests made on air-dried samples can give markedly different results than tests on samples at their natural water content.

## Slide 33: 1.5 2:1 Minerals-Montmorillonite
n·H2O+cations
5 m
Si8Al4O20(OH)4·nH2O (Theoretical unsubstituted). Film-like shape.
There is extensive isomorphous substitution for silicon and aluminum by other cations, which results in charge deficiencies of clay particles.
n·H2O and cations exist between unit layers, and the basal spacing is from 9.6 Å to  (after swelling).
The interlayer bonding is by van der Waals forces and by cations which balance charge deficiencies (weak bonding).
There exists interlayer swelling, which is very important to engineering practice (expansive clay).
(Holtz and Kovacs, 1981)
Notes: Montmorillonite is the dominant clay mineral in bentonite, altered from volcanic ash. Bentonite has the unsual property gives rise to interesting industrial used. Most important is as drilling mud in which the montmorillonite is used to give the fluid viscosity several times that of water. It is also used for stopping leakage in soil, rocks, and dams.

## Slide 34
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Atomic structure of montmorillonite (after Grim 1959

## Slide 35: 1.5 2:1 Minerals-Illite (mica-like minerals)
potassium
Si8(Al,Mg, Fe)4~6O20(OH)4·(K,H2O)2. Flaky shape.
The basic structure is very similar to the mica, so it is sometimes referred to as hydrous mica. Illite is the chief constituent in many shales.
Some of the Si4+ in the tetrahedral sheet are replaced by the Al3+, and some of the Al3+ in the octahedral sheet are substituted by the Mg2+ or Fe3+. Those are the origins of charge deficiencies.
The charge deficiency is balanced by the potassium ion between layers. Note that the potassium atom can exactly fit into the hexagonal hole in the tetrahedral sheet and form a strong interlayer bonding.
The basal spacing is fixed at 10 Å in the presence of polar liquids (no interlayer swelling)
7.5 m
K
Notes: (1)Fewer of Si4+positions are filled by Al3+ in the illite.
(2)There is some randomness in the stacking of layers in illite.
(3) There is less potassium in illite. Well-organized illite contains 9-10% K2O.
(4) Illite particles are much smaller than mica particles.
Ferric ion Fe3+

## Slide 36
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Atomic structure of illite

## Slide 37: 1.5 2:1 Minerals-Vermiculite (micalike minerals)
The octahedral sheet is brucite.
The basal spacing is from 10 Å to 14 Å.
It contains exchangeable cations such as Ca2+ and Mg2+ and two layers of water within interlayers.
It can be an excellent insulation material after dehydrated.
Illite
Vermiculite
Notes: Vermiculite is similar to montmorillonite, a 2:1 mineral, but it has only two interlayers of water. After it is dried at high temperature, which removes the interlayer water, expanded” vermiculite makes an excellent insulation material.

## Slide 38
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Diagram of the structures of (a) kaolinite; (b) illite; (c) montmorillonite

## Slide 39: 1.8 Mixed Layer Clays
Different types of clay minerals have similar structures (tetrahedral and octahedral sheets) so that interstratification of layers of different clay minerals can be observed.
In general, the mixed layer clays are composed of interstratification of expanded water-bearing layers and non-water-bearing layers. Montmorillonite-illite is most common, and chlorite-vermiculite and chlorite-montmorillonite are often found.
(Mitchell, 1993)
Notes: Most than one type of clay mineral is usually found in most soils. Because of the great similarity in crystal structure among the different minerals, interstratification of two or more layer types often occurs within a single particle
The most abundant mixed layer material is composed of expanded water-bearing layers and contracted non-water-bearing layers. Montmorillonite-illite is most common, and chlorite-vermiculite and chlorite-montmorillonite are often found

## Slide 40: 2. Identification of Clay Minerals

## Slide 41: 2.1 X-ray diffraction
The distance of atomic planes d can be determined based on the Bragg’s equation.
BC+CD = n, n = 2d·sin, d = n/2 sin
where n is an integer and  is the wavelength.
Different clays minerals have various basal spacing (atomic planes). For example, the basing spacing of kaolinite is 7.2 Å.
Mitchell, 1993
Notes: Electronmicroscopy, both transmission and scanning, can be used to identify clay minerals in a soil sample, but the process is not easy and/or quantitative.
Bragg’s law: The two rays will constructively interfere if the extra distance ray I travels is a whole number of wavelengths farther then what ray II travels.

## Slide 42: 2.3 Other Methods
Electron microscopy
Specific surface (Ss)
Cation exchange capacity (cec)
Plasticity chart

## Slide 43: 2.3 Other Methods (Cont.)
5. Potassium determination
Well-organized 10Å illite layers contain 9% ~ 10 % K2O.
6. Thermogravimetric analysis
  It is based on changes in weight caused by loss of water or CO2 or gain in oxygen.
  Sometimes, you cannot identify clay minerals only based on one method.

## Slide 44
Scanning electron micrograph of a kaolinite specimen (courtesy of U.S. Geological Survey)

## Slide 45: 3. Specific Surface (Ss)

## Slide 46: 3.1 Definition
Example:
Surface related forces: van der Waals forces, capillary forces, etc.
Ss is inversely proportional to the particle size
Preferred
Notes: Demonstration of capillary force between Large particle and small particle.

## Slide 47: 3.2 Typical Values
Montmorillonite
Illite
Kaolinite
50-120 m2/g (external surface)
700-840 m2/g (including the interlayer surface)
65-100 m2/gm
10-20 m2/gm
Interlayer surface
Notes: Say something about the engineering applications and the specific surface

## Slide 48: 4. Interaction of Water and Clay Minerals

## Slide 49: 4.1 Origins of Charge Deficiencies
Imperfections in the crystal lattice -Isomorphous substitution.
  The cations in the octahedral or tetrahedral sheet can be replaced by different kinds of cations without change in crystal structure (similar physical size of cations).
  For example,
  Al3+ in place of Si4+ (Tetrahedral sheet)
  Mg2+ instead of Al3+(Octahedral sheet)
  unbalanced charges (charge deficiencies)
  This is the main source of charge deficiencies for montmorillonite.
  Only minor isomorphous substitution takes place in kaolinite.
Notes: Common examples are aluminum in place of silicon, magnesium instead of aluminum, and ferrous iron (Fe2+) for magnesium. This presence in an octahedral or tetrahedral position of a cation other than that normally found, without change in crystal structure, is isomorphous substitution.

## Slide 50: 4.2 Origins of Charge Deficiencies (Cont.)
2. Imperfections in the crystal lattice - The broken edge
The broken edge can be positively or negatively charged.

## Slide 51: 4.2 Origins of Charge Deficiencies (Cont.)
3. Proton equilibria (pH-dependent charges)
Kaolinite particles are positively charged on their edges when in a low pH environment, but negatively charged in a high pH (basic) environment.
M
M
M
O
O-
O
H+
H
H
M: metal

## Slide 52: 4.2 Origins of Charge Deficiencies (Cont.)
4. Adsorbed ion charge (inner sphere complex charge and outer sphere complex charge)
  Ions of outer sphere complexes do not lose their hydration spheres. The inner complexes have direct electrostatic bonding between the central atoms.

## Slide 53: 4.3 “Charged” Clay Particles
External or interlayer surfaces are negatively charged in general.
The edges can be positively or negatively charged.
Different cations balance charge deficiencies.
Dry condition
- or +
- or +
Cation
Kaolinite and negative gold sol (gold colloid, nano-particle)
(van Olphen, 1991)

## Slide 54
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Dipolar character of water

## Slide 55: 4.4 Polar Water Molecules
Structure
Polar molecule
H(+)
H(+)
O(-)
Hydrogen bond
Salts in aqueous solution
hydration
Notes: Salts dissolve in water

## Slide 56
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Attraction of dipolar molecules in diffuse double layer

## Slide 57: 4.5 Clay-Water Interaction
Adsorbed layers
3 monolayers
1. Hydrogen bond
Kaolinite
Oxygen
Hydroxyl
Clay Surfaces
Free water
Bulk water
The water molecule “locked” in the adsorbed layers has different properties compared to that of the bulk water due to the strong attraction from the surface.
O
OH
H
O
H
O
H
O
H
H

## Slide 58: 4.5 Clay-Water Interaction (Cont.)
The water molecules wedge into the interlayer after adding water
2. Ion hydration
Dry condition
(Interlayer)
Clay layers
cation
The cations are fully hydrated, which results in repulsive forces and expanding clay layers (hydration energy).
Na+ crystal radius: 0.095 nm
radius of hydrated ion: 0.358 nm

## Slide 59: 4.5 Clay-Water Interaction (Cont.)
The concentration of cations is higher in the interlayers (A) compared with that in the solution (B) due to negatively charged surfaces. Because of this concentration difference, water molecules tend to diffuse toward the interlayer in an attempt to equalize concentration.
3. Osmotic pressure
From Oxtoby et al., 1994
A
B

## Slide 60
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Clay water (redrawn after Lambe, 1958

## Slide 61: 5. Interaction of Clay Particles (or Layers)
Interlayer
Interparticle
Layer
Particle

## Slide 62: 5.1 Diffuse Double Layer
Clay particle with negatively charged surface
x
Distance x
Concentration
Exponential decay
Cations
Anions
-
-
+
+
-
-
-
-
-

## Slide 63
(c)2001 Brooks/Cole, a division of Thomson Learning, Inc. Thomson Learning™ is a trademark used herein under license.
Diffuse double layer

## Slide 64: 5.2 Interaction Forces
Net force between clay particles (or interlayers)
= van der Waals attraction +
Double layer repulsion (overlapping of the double layer)+
Coulombian attraction (between the positive edge and negative face)
DLVO forces

## Slide 65: 5.3 Thickness of Double Layer
Thickness of double layer K
K  repulsion force 
n0 K  repulsion force 
v  K  repulsion force 
T  K  repulsion force (?)
 decreases with increasing temperature

## Slide 66: 5.4 Interaction of Clay Particles
Dispersed fabric
The net interparticle force between surfaces is repulsive
Increasing
Electrolyte concentration n0
Ion valence v
Temperature T (?)
Decreasing
Permittivity 
Size of hydration ion
pH
Anion adsorption
Reduce the double layer repulsion (only applicable to some cases)
Flocculated or aggregated fabric
Flocculated fabric
Edge-to-face (EF): positively charged edges and negatively charged surfaces (more common)
Edge-to-edge (EE)
Aggregated fabric
Face-to-Face (FF)
Shifted FF
Notes: If the net effect of the attractive and repulsive forces between the two clay particles is attractive, the two particles will tend to move toward each other and become attached-flocculate. If the net influence is repulsive they tend to move away-disperse

## Slide 67: 5.4 Interaction of Clay Particles (Cont.)
(1) Decrease pH
(2) Decrease anion adsorption
(3)Size of hydration
Clay Particle
The total required number of cations is 10
+
+
-
-
-
-
-
-
-
-
-

## Slide 68: 5.5 Atterberg Limit of Clay Minerals
Lambe and Whitman, 1979
Na-montmorillonite
Thicker double layer
LL=710
Ca-montmorillonite
Thinner double layer
LL=510
The thickness of double layer increases with decreasing cation valence.
Notes: Put the table of LL and PL for different clay minerals again (in the Mitchell’s book)****

## Slide 69: 5.6 Cation Replaceability
Different types and quantities of cations are adsorbed to balance charge deficiencies in clay particles.
The types of adsorbed cations depend on the depositional environment. For example, sodium and magnesium are dominant cations in marine clays since they are common in sea water. In general, calcium and magnesium are the predominant cations.
The adsorbed cations are exchangeable (replaceable). For example,
Na
Na
Na
Na
Na
Na
Na
Na
+4CaCl2 
+8NaCl
Ca
Ca
Ca
Ca
(Lambe and Whitman, 1979)
Notes: The number of exchangeable charges is the “counterion exchange capacity (CEC) of the mineral. Clearly, it is related to surface charge density and specific surface
In units of Coulombs per gram (C/g) or in terms of milliequivalents per gram (meq/g)

## Slide 70: 5.6 Cation Replaceability (Cont.)
The ease of cation replacement depends on the
(1) Valence (primarily)
  Higher valence cations can replace cations of lower valence.
(2) Ion size
  Cations with larger non-hydrated radii or smaller hydrated radii have greater replacement power.
According to rules (1) and (2), the general order of replacement is
Li+<Na+<K+<Rb+<Cs+<Mg2+<Ca2+<Ba2+<Cu2+<Al3+<Fe3+<Th4+
(3) Relative amount
  High concentration of Na+ can displace Al3+.
Cations
Non-hydrated radius (Å)
Hydrated radius (Å)
Li+
0.68
3.8
Na+
0.95
3.6
K+
1.33
3.3
Cs+
1.69
3.3
Be2+
0.31
4.6
Mg2+
0.65
4.3
Ca2+
0.99
4.1
Ba2+
1.35
Al3+
0.5
4.8
Fe3+
0.6
(Data compiled from Israelachvili, 1991)
Notes: Calcium

## Slide 71: 5.7 Cation Exchange Capacity (cec)
The quantity of exchangeable cations is termed the cation exchangeable capacity (cec) and is usually expressed as milliequivalents (meq) per 100 gram of dry clay ( from Mitchell, 1993).
One equivalent = 6.021023 electron charges or 96500 Coulombs, which is 1 Faraday.

## Slide 72: 5.8 Swelling Potential
Practically speaking, the three ingredients generally necessary for potentially damaging swelling to occur are (1) presence of montmorillonite in the soil, (2) the natural water content must be around the PL, and (3) there must be a source of water for the potentially swelling clay (Gromko, 1974, from Holtz and Kovacs, 1981)
Holtz and Kovacs, 1981
U.S. Bureau of Reclamation

## Slide 73: 5.9 Engineering Applications
Lime treatment for the swelling clay
The swelling clay such as Na-montmorillonite beneath the foundation is potentially harmful to the light structure. Adding lime (CaO) into such soil can effectively reduce the swelling potential due to Ca2+ displacing Na+, and can increase the strength by dehydration of soils and cementation.
Drilling mud
Soil particle
The swelling clays can form a so-called “filter cake” and enable soil layers to become relatively impermeable.
Earth pressure+ ground water pressure
Pressure profile of slurry
Trench
Bentonite or
Polymer
Montmorillonite is the dominant clay mineral in bentonite
Xanthakos, 1991
Notes: Also can be used for sealing an rock cavern in which the nuclear waste is stored.
Bentonite. See Mitchell’s book , page 32.

## Slide 74: 5.9 Engineering Applications (Cont.)
Xanthakos, 1991

## Slide 75: 5.9 Engineering Applications (Cont.)
Xanthakos, 1991

## Slide 76: 5.9 Engineering Applications
Dispersion agents (drilling mud; hydrometer analysis)
Sodium hexa-metaphosphate (NaPO3) and sodium silicate (Na2SiO3) are used as the dispersion agent in the hydrometer analysis. How does this dispersion agent work?
Three hypotheses:
(1) Edge-charge reversal
The anions adsorption onto the edge of the clay particle may neutralize the positive edge-charge or further reverse the edge-charge from positive to negative. The edge-charge reversal can form a negative double layer on the edge surfaces to break down flocculated structure, and assist in forming a dispersed structure.
(2) Ion exchange
The sodium cations can replace the divalent cations existing in the clay particles such as Ca2+ and Mg2+. The decrease of cation valence can increase the thickness of the double layer and interparticle repulsion, which can assist in forming a dispersed structure.
(3) pH
The higher pH may make the edge-charge tend to be negative, which can break down the flocculated structure and assist in forming a dispersed structure. The adding of dispersing agent such as sodium carbonate may slightly increase the pH.

## Slide 77: 6. Soil Structure and Fabric

## Slide 78: 6. Soil Structure and Fabric
The structure of a soil is taken to mean both the geometric arrangement of the particles or mineral grains as well as the interparticle forces which may act between them.
Soil fabric refers only to the geometric arrangement of particles (from Holtz and Kovacs, 1981).
The interparticle forces (or surface forces) are relatively important for fine-grained soils at low confinement (low state of stress).
“Although the behavior of a coarse-grained soil can often be related to particle size distribution, the behavior of a fined-grained soil usually depends much more on geological history and structure than on particle size” (from Lambe and Whitman, 1979).
*Fabric and structure are used interchangeably sometimes.

## Slide 79: 7. Soil Fabric-Natural Soil (fine-grained soils)

## Slide 80: 7.1 Microfabric Features in Natural Soils
Elementary particle arrangements, which consist of single forms of particle interaction at the level of individual clay, silt, or sand particles or interaction between small groups of clay platelets or clothed silt and sand particles.
Particle assemblages, which are units of particle organization having definable physical boundaries and a specific mechanical function. Particle assemblages consist of one or more forms of elementary particle arrangements or smaller particle assemblages.
Pore spaces within and between elementary particles arrangements and particle assemblages.
Collins and McGown, 1974 (from Holtz and Kovacs, 1981)

## Slide 81: 7.1 Elementary Particles
Individual clay platelet interaction
Individual silt or sand particle interaction
Clay platelet group interaction
Clothed silt or sand particle interaction
Particle discernible
Collins and McGown, 1974 (from Holtz and Kovacs, 1981)

## Slide 82: 7.2 Particle Assemblages
Collins and McGown, 1974 (from Holtz and Kovacs, 1981)

## Slide 83: 7.3 Pore Space Types
Collins and McGown, 1974 (from Mitchell, 1993)

## Slide 84: 8. Soil Fabric-Clay Soils

## Slide 85: 8.1 Terminology
Dispersed: No face-to-face association of clay particles
Aggregated: Face-to-face association (FF) of several clay particles.
Flocculated: Edge-to-Edge (EE) or edge-to-face (EF) association
Deflocculated: No association between aggregates
Face (F)
Edge (E)
Clay Particle
van Olphen, 1991 (from Mitchell, 1993)

## Slide 86: 8.2 Particle Associations
Dispersed and deflocculated
Aggregated but deflocculated
Edge-to-face flocculated and aggregated
Edge-to-edge flocculated and aggregated
Edge-to-face and edge to edge flocculated and aggregated
Edge-to-edge flocculated but dispersed
Edge-to-face flocculated but dispersed
van Olphen, 1991

## Slide 87: 8.3 Summary
Flocculated fabric
Dispersed fabric
Edge-to-face (EF): positively charged edges and negatively charged surfaces (more common)
Edge-to-edge (EE)
The net interparticle force between surfaces is repulsive
Aggregated fabric
Face-to-Face (FF)
Shifted
Face-to-Face (FF)
Notes: If the net effect of the attractive and repulsive forces between the two clay particles is attractive, the two particles will tend to move toward each other and become attached-flocculate. If the net influence is repulsive they tend to move away-disperse

## Slide 88: 8.4 Fabric of Natural Clay Soils
“The individual clay particles seem to always be aggregated or flocculated together in submicroscopic fabric units called domains. Domains then in turn group together to form clusters, which are large enough to be seen with a visible light microscope. Clusters group together to form peds and even groups of peds. Peds can be seen without a microscope, and they and other macrostructural features such as joints and fissures constitute the macrofabric system” (from Holtz and Kovacs, 1981).
Domain  Cluster Ped

## Slide 89: 8.4 Fabric of Natural Clay Soils (Cont.)
Enlargement
Domains and clusters with micropores
Domain
Cluster
Ped
Silt grain
Micropore
Macropore
Yong and Sheeran (1973) (from Holtz and Kovacs, 1981)

## Slide 90: 9. Soil Fabrics-Granular Soils

## Slide 91: 9.1 Packing
Dense packing
Loose packing
Honeycombed fabric
Meta-stable structure
Loose fabric
Liquefaction
Sand boil
Holtz and Kovacs, 1981

## Slide 92: 9.1 Packing (Cont.)-Sand Boil
Loose sand
Kramer, 1996

## Slide 93: 9.1 Packing (Cont.)
“Contrary to popular belief, it is not possible to drown in quicksand, unless you really work at it, because the density of quicksand is much greater than that of water. Since you can almost float in water, you should easily be able to float in quicksand “(from Holtz and Kovacs, 1981).
Help!

## Slide 94: 9.2 Load Transfer
Loading
The black particles carry most of load. The remaining particles prevent the buckling of the load-carrying chains (From Santamarina et al., 2001).

## Slide 95: HW#1 (Soil formation & Fabrics)
1.a) What is a mineral?
b) Describe the differences among the three main clay minerals.
c) Why are silicates the most common minerals?
2.Describe the following types of bonding agents found with clay minerals.
a)Hydrogen bond
b)Van der Waals’ forces
3.Describe briefly the crystalline or atomic structure of the following minerals. Also list any important distinguishing characteristics.
a) Gibbsite b) Bentonite c)Illite d)Halloysite e) Chlorite
4.a) What is soil fabric?
b) What is the name for spaces between mineral particles?
c) Why are the spaces between mineral particles important to geoengineers?
d) Explain the differences between a flocculated and a dispersed structure.