## Slide 1: Consolidation

## Slide 2
Higher compressibility

## Slide 3: Soil Settlement and Compression
Immediate Settlement
  Elastic deformation, undrained compression (sands, gravels)
Primary Consolidation
  Time dependent settlement in saturated soil as water is squeezed from voids due to increase in vertical effective stress (clays)
Secondary Consolidation
  Particle reorientation, creep, organic decay; does not involve expulsion of water (highly plastic clays, organics)
Distortion Settlement
  Lateral movements near edges of loaded area

## Slide 4: Changes in Vertical Effective Stress
Fill Placement
External Loading
Water Table Changes
Combinations of 1, 2, and 3
Hfill
gfill
P
sz’
sz’
sz’
sz’
(e.g., water table lowering)

## Slide 5: Subsidence from Water Table Lowering
  Example:
Initial GWT
Final GWT
5m
5m
A
USGS
g = 20 kN/m3
san joaquin valley

## Slide 6: Primary Consolidation: Piston-Spring Analogy
1. The container is completely filled with water, and the hole is closed. (Fully saturated soil)
2. A load is applied onto the piston, while the hole is still unopened. At this stage, only the water resists the applied load. (Development of excess pore water pressure-Undrained Condition)
3. As soon as the hole is opened, water starts to drain out through the hole and the spring shortens. (Drainage and dissipation of excess pore water pressure)
4. After some time, the drainage of water no longer occurs. Now, the spring alone resists the applied load. (Full dissipation of excessive pore water pressure. Drained condition, End of consolidation)

## Slide 7
Spring is analogous to soil skeleton (effective stress)
Initially, the pore water takes up the change in total stress so effective stress does not change
As excess pore water pressure drains, the effective stress increases (skeleton takes up load)
Consolidation is complete when excess pressure dissipates and flow stops
So consolidation is TIME DEPENDENT because it is a pressure dissipation (flow) process!
Depends on hydraulic conductivity (k) and length of drainage path (Hdr)
Flow
P

## Slide 8
Example 11.2 (Coduto, 1999)
Before Fill:
Short Term After Fill:
Long Term After Fill:

## Slide 9: Consolidation (Oedometer) Testing
1-D consolidation test:
  Undisturbed saturated soil (clay, silt) – representative of in-situ stratum
  Typical specimen size: h = 1”, diam. = 2”-3”
  Specimen confined in rigid ring (no lateral deformation, “plane strain”)
  Drainage allowed on top and bottom via porous stones
  Apply increment of load and measure 1-D compression with time

## Slide 10: Trimming Procedures
(Bardet, 1997)

## Slide 11: Assumptions
All compression occurs due to change in void ratio
  i.e., the grains do not compress
  Thus, we can relate change in void ratio (e) to change in volume
2) All strains are vertical (1-D)
H0
DH
e0

## Slide 12: Procedures for Incremental Consol Testing
Trimming
Specimen set up and initialization (seating load, s’v0)
Apply an increment of vertical load (s’v = P/A)
Record DH with time, compute De with time
Monitor until volume change ceases (~24 h)
Repeat 3-5 to generate load-compression curve
time
e0
e1
e2
en
1st increment
2nd
nth
~24h
e0
e1
e2
en
log s’v
s’v0
s’v1
s’v2
s’vn
We will use this data to predict magnitude of consolidation settlement
We will use this data to predict rate of consolidation
“e-log p” curve

## Slide 13: The “e-log p” curve
San Francisco Bay Mud (Holtz and Kovacs, 1981)
Loading
Unoading
Loading
Unloading

## Slide 14
Virgin (NC)
Compression
Cc
Cs
Cr
s’c
OC Compression
A
Divide e-log p curve into linear segments
OC = Overconsolidated (stiff response)
NC = Normally Consolidated (soft response)
OC and NC portions separated by s’c
s’p = “maximum past pressure”
Cr = Recompression Index (slope of OC)
Cc = Compression Index (slope of NC)
Cs = Swell Index (slope of unload response)
B
C
D
0.1 ~ Cc ~ 2.6
0.01 ~ Cr ~ 0.5

## Slide 15
(Bardet, 1997)

## Slide 16: Stress History
NC
Cc
Cs
Cr
s’c
OC
A
Maximum past pressure (s’p ) quantifies
The “stress history” of the soil – it is the largest magnitude of effective stress the soil has been consolidated to in the past.
Overconsolidation Ratio (OCR) quantifies the magnitude of a soil’s existing state of stress relative to its maximum past stress.
B
C
D
If OCR = 1, then s’p = s’ and the soil is “normally consolidated” (soft response – virgin compression)
If OCR > 1, then s’p > s’ and the soil is “over consolidated” (stiff response – it has been precompressed)
Sources of Overconsolidation:
  Extensive erosion
  Past glacial activity
  Removed structures
  Risen water table
  Evaporation

## Slide 17: Disturbance & Empirical Correlations
For NC or undisturbed specimens:
For OC or disturbed specimens:
(Disturbance decreases virgin compressibility)
In general:
Disturbance “erases” stress history

## Slide 18: Load-Rebound Behavior
Maximum past stress (aka preconsolidation
Stress) is a plastic yield stress.
If unloading occurs at a stress less than s’c, then the soil rebounds elastically.
If unloading occurs at a stress greater than s’c, then a new s’c results and the soil rebounds plastically.
A
B
C
eA
ec
s’A = s’C
s’B
s’c
Similar to elastic-plastic response you learned about in Mechanics of Materials
s
e
yield
stress
plastic deformation

## Slide 19: DETERMINATION OF MAXIMUM PAST PRESSURE
14.330 SOIL MECHANICS Consolidation
(´c or ´vm)
Graphical Method (Casagrande, 1936)
Visually identify point of minimum radius of curvature on e-log ´ curve (i.e. Point a).
Draw horizontal line from Point a
(i.e. Line ab).
Draw Line ac tangent to Point a.
Draw Line ad bisecting Angle bac.
Project the straight line portion of gh on e-log ´ curve to intersect Line ad. This intersection (Point f) is the maximum past pressure (a.k.a. preconsolidation pressure).

## Slide 20: Calculating Consolidation Settlement
Site characterization to quantify thickness of compressible layer.
1-D laboratory consolidation testing to determine stress history and compression indices (s’c, Cc, Cr, Cs). Will also need cv for rate prediction.
Divide compressible layer into sublayers.
Calculate initial (preconstruction) effective vertical stress at midpoint of each sublayer (s’i).
Calculate final post-construction effective vertical stress at midpoint of each sublayer (s’f=s’i+ Δs’)
Calculate consolidation settlement for each sublayer (DH) and sum for total settlement.
gfill
Fill
Soft
Clay
Rock
1
2
3
4
H1
H2
H3
H4

## Slide 21
Calculating Consolidation Settlement

## Slide 22
Where did those equations come from?
NC
Cc
Cs
Cr
s’c
OC
s’i
s’f
e0
ef
De

## Slide 23: Example – Fill Placement
Prop. | A | B
Cc | 0.25 | 0.20
Cr | 0.08 | 0.06
e0 | 0.66 | 0.45
s’c | 101 kPa | 510 kPa
See Coduto for solution using 7 layers
Let’s try using two layers (A and B)
B
A
4.5 m
9 m
Compare to max past stress:
e
Log s’
233
101
60
Need both terms

## Slide 24
Prop. | A | B
Cc | 0.25 | 0.20
Cr | 0.08 | 0.06
e0 | 0.66 | 0.45
s’p | 101 kPa | 510 kPa
Compare to max past stress:
e
Log s’
361
510
188
Only need
Cr term
Now for layer B:
Compare to solution for 7 layers…. DHtot = 0.83 m

## Slide 25: Rate of Consolidation Settlement
Recall that consolidation is volume change due to pore water being squeezed out
Dissipation of excess pore pressure
So consolidation takes time!!! – depends on:
  Hydraulic conductivity (k)
  Drainage boundaries (max length of drainage path, Hdr)
gfill
Fill
Soft
Clay
Rock
k
Hdr
z
Static Pressure
us
+
+
=
z
Excess Pressure
u
z
u
Transient
Profile
Immediate
Long
Term

## Slide 26
Consider a case of double-drainage (like an oedometer test)
Top porous disk
Saturated
Clay
Bottom porous disk
H0
Ds
z
Ds
So there is a hydraulic gradient from middle of sample to boundaries
The magnitude of the gradient decreases with time
So flow rate decreases with time
So rate of volume change decreases with time
Volume
Time
We want to be able to plan for this!

## Slide 27
Drainage Path Length, Hdr
Saturated
Clay
Flow rate (rate of consolidation) depends on k and dht/dL
Hdr = H0
Impervious Rock,
Aquitard, etc.
Ground surface, sand layer, etc.
Single Drainage
Saturated
Clay
Hdr = ½ H0
Pervious layer, sand, etc.
Ground surface, sand layer, etc.
Double Drainage
Significantly decreases time for consolidation

## Slide 28: TIME RATE OF CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
Clay Layer Undergoing Consolidation
Figure 7.17a. Das FGE (2005).
Theory of 1D Consolidation (Terzaghi, 1925)
Assumptions:
The clay-water system is homogenous.
Saturation is complete (S = 100%).
Compressibility of water is negligible.
Compressibility of soil grains is negligible (but soil particles rearrange).
Flow of water is in one direction only.
Darcy’s Law is Valid.

## Slide 29
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).
Clay Layer Undergoing Consolidation
Figure 7.17a. Das FGE (2005).
TIME RATE OF CONSOLIDATION

## Slide 30: TIME RATE OF CONSOLIDATION (Rate of Water Outflow) –
14.330 SOIL MECHANICS Consolidation
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).
or
dt
z
z
z dt
vz dxdydz  V
dxdy 
dz dxdy  v





 v
z
vz V
(Rate of Water Inflow) =
(Rate of Volume Changes)
Mathematical Equation:
Where:
V = Volume of Soil Element
vz = Velocity of flow in z direction

## Slide 31: TIME RATE OF CONSOLIDATION
Slide 41 of 74
Revised 03/2013
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).
Where:
Vs = Volume of Solids
vv = Volume of Voids
s
w
z
e  e Vs
t t
V
t t t t
V  Vv  Vs  eVs   Vs
dxdydz t
z2
u
v  ki  k h   k
z t
vz dxdydz  V
 w
z  z
Using Darcy’s Law (v = ki)
Where u = excess pore pressure. From algebra:
 k 2u  1 V
Rate of change in V = Rate of Change in Vv

## Slide 32: TIME RATE OF CONSOLIDATION
Slide 42 of 74
Revised 03/2013
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).
s
s
1 eo t
z2
1eo 1 eo
V 
 0
t
Vs
e  e Vs
t t
V
V  Vv  Vs  eVs   Vs
t t t t
 w
From Previous Slide
Assuming soil solids are incompressible
and
V  dxdydz
eo = Initial Void Ratio. Substituting:
V  dxdydz e
t 1 eo t
Combining equations:
 k 2u  1 e

## Slide 33: TIME RATE OF CONSOLIDATION
Slide 43 of 74
Revised 03/2013
14.330 SOIL MECHANICS Consolidation
o
v
w o
av
m 
u
k av
1  e
1  e t mv t
1  eo t
z2
2u   u  
z2
 k 2u  1 e

 w
From Previous Slide
The change in void ratio is caused by the increase in effective stress.
Assuming linear relationship between the two:
e  av   avu
av = Coefficient of Compressibility. Can be considered constant over narrow pressure increases.
Combining equations:
mv = Coefficient of Volume Compressibility.
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).

## Slide 34: TIME RATE OF CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
w v
o
v
w o
m 
av

cv  
t
m 
u
u  
k av
cv z2
z2
2u  
1  e
1  e t mv t
From Previous Slide
Rearranging Equations:
u  2u
av = Coefficient of Compressibility.
mv = Coefficient of Volume Compressibility.
Where cv = Coefficient of Consolidation.
k
Flow of Water @ Point A
Figure 7.17b. Das FGE (2005).

## Slide 35: TIME RATE OF CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
cv z2
t
Basic Differential Equation of 1D Consolidation Theory
u  2u
Can be solved with the following boundary conditions:
z  0, u  0
z  2Hdr , u  0
t  0, u  u0
The solution yields
v
o
sin
M 2T


m0  M
m 2u
 e
 Hdr 
 Mz 
u 
Clay Layer Undergoing Consolidation
Figure 7.17a. Das FGE (2005).

## Slide 36: TIME RATE OF CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
v
cvt
T 
H 2dr
2
uo  Initial excess pore water pressure
M   2m  1
Clay Layer Undergoing Consolidation
Figure 7.17a. Das FGE (2005).
Where:
 TIME FACTOR

## Slide 37: TIME RATE OF CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
o
o
z
u
u
U
 uo  uz
 1  uz
Consolidation progresses by dissipation of excess pore pressure, the degree of consolidation Uz at a distance z at any time t is defined as:
Clay Layer Undergoing Consolidation

## Slide 38
Slide 48 of 74
Revised 03/2013
TIME RATE OF CONSOLIDATION

## Slide 39: TIME RATE OF CONSOLIDATION
Revised 03/2013
Average degree of consolidation (U)
for the entire depth of the clay layer at any time t is:
Where:
U  Average degree of Consolidation
Substituting U for u
U can be approximated by the following relationships:
Clay Layer Undergoing Consolidation

## Slide 40
Slide 51 of 74
Revised 03/2013
Figure 7.28. Das FGE (2006).
TIME RATE OF CONSOLIDATION
Difference between Average Degree of Consolidation and Midplane Degree of Consolidation

## Slide 41
Slide 50 of 74
Revised 03/2013
TIME RATE OF CONSOLIDATION

## Slide 43
Example 1: How long for 90% consolidation?
From figure, T = 0.848
Clay
cv = 0.05 ft2/day
20’
Sand

## Slide 44
If S∞ = 4.0’, how long for 2’ of settlement?
From figure, T = 0.196
Clay
cv = 0.05 ft2/day
20’
Sand

## Slide 45
If bottom boundary is impervious, how long for 90% consolidation?
From figure, T = 0.848
Clay
cv = 0.05 ft2/day
20’
Impervious Rock

## Slide 46
Compute total consolidation settlement and time for 95% consolidation
OCR = 1, so clay is NC.
Clay
k = 10-6 cm/s
e0 = 1.2
Cc = 0.40
G = 100 pcf
OCR = 1
50’
Impervious Rock
20’
Prop. fill
g= 100pcf
Analyze using Point A at midpoint of clay
A
25’

## Slide 47
Not given cv, so need to calculate…
Clay
k = 10-6 cm/s
e0 = 1.2
Cc = 0.40
G = 100 pcf
OCR = 1
50’
Impervious Rock
20’
Prop. fill
g= 100pcf
A
25’
If U = 95%, T = 1.129

## Slide 48
DH =
Cc H
1 + eO
P0
Po + DP
log ( )
Dp
Dp
Dp
Dp
Dp
Dp

## Slide 49
Dp
Dp
Dp2
Dp2
Dp2
Dp
Dp
DH = log ( ) +
CS H
1 + eO
PC
Po
C C H
1 + eO
PC
Po + DP
log ( )
2
2

## Slide 50
Dp
Dp2
Dp2
Dp2
Dp2
DH = log
CS H
1 + eO
Po
Po + DP
( )
2

## Slide 51
Chart: 
| 1 | 1
 | 1000 | 1000
Log (σ’)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Sand
Clay
σ’o
Soil sample was obtained from the clay layer
Conduct consolidation test [9 load increments ]
Plot e vs. log (p) (Figure 2)
Determine Compression Index (Cc ) & Swelling Index (Cs)
Example:
Figure 2
Figure 1
Soil Sample
Cc
Cs
Dp
Dp7
Dp
Dp1
Dp9
In the lab and after removing
the soil sample from the ground,
the stresses on the soil sample = 0
In the lab the stresses are
added to the soil sample
Dp1
Dp9
Stress
Increments
eo = 0.795
Dp2
In the ground, the sample was subjected to geostatic stresses.
In the lab and before the consolidation test the stresses on the sample = 0.
During testing, the geostatic stress is gradually recovered
Cc = 0.72
Cs = 0.1
Dr. Kamal Tawfiq - 2010
σ’o

## Slide 52
Chart: 
| 1 | 1
 | 1000 | 1000
Log (σ’)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Sand
Clay
X
X
σ’c
Determine:
σ’= 3.(96) + 4.(96-62.4) + 8.(110-62.4) = 803.2 lb/ft2
6. Using Casagrande’s Method to determine σ’c
σ’c = 800 lb/ft2
Overconsolidation Ratio
OCR = = 1
The soil is
Normally Consolidated
N.C. soil
Example (cont.)
Dp1
σ’c
σ’o
1
2
3
4
5
6
Point of
maximum curvature
Tangent to point 1
Tangent to point 1
7
Dr. Kamal Tawfiq - 2010

## Slide 53
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
σ’c
A 150’ x 100’ building will be constructed at the site.
The vertical stress due to the addition of the building
qdesign =1000 lb/ft2
The weight of the building Qdesign will be transferred
to the mid height of the clay layer
Qdesign = 15,000,000 lb
The added stress at 15’ from
the ground surface is
D σ’ =
Example (cont.)
Dp1
Building
qdesign
Po
DP1
G.S.
(150+15) x (100+15)
15,000,000 lb
D σ’ = 790.51 lb/ft2
D σ’ + σ’o =
790.51 + 803 = 1593.51 lb/ft2
Dr. Kamal Tawfiq - 2010

## Slide 54
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Sand
Clay
σ’o
Example: (cont.)
Dp1
Building
qdesign
G.S.
Consolidation Settlement
DH = log ( )
Cc H
1 + eO
D σ’ + σ’o
σ’o
D σ’ + σ’o
D σ’
DH = log ( )
0.72 x 16
1 + 0.795
1593.51
803
DH = 1.9 ft
D σ’ + σ’o = 790.51 + 803 = 1593.51 lb/ft2
σ’o
D σ’

## Slide 55
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Sand
Clay
Dp1
qdesign
G.S.
When the building was removed, the soil has become
an overconsolidated clay.
The rebound has taken place through
swelling from pint 1 to point 2
2
1
Demolished
Dr. Kamal Tawfiq - 2010
σ’o
D σ’ + σ’o
D σ’

## Slide 56
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Sand
Clay
Dp1
qdesign
G.S.
DP2
New Building
CS
CC
DH = log ( ) +
CS H
1 + eO
σ’c
σ’o
C C H
1 + eO
σ’c
D σ’ + σ’o
log
Scenario #1
The soil now is overconsolidated Soil:
The new building is heavier in weight
σ’c
Constructing a new building
eo = 0.61
Assume
D σ’ + σ’o=2100 psf
DH =
0.1 x 16
1 + 0.61
1593.51
803
log
( )
+
0.72 x 16
1 + 0.61
1593.51
log
( )
2100
=1.15 ft
Dr. Kamal Tawfiq - 2010
σ’o
D σ’ + σ’o
D σ’

## Slide 57
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Sand
Clay
Scenario # 2
The soil now is overconsolidated Soil:
The new building is lighter in weight
Dp1
qdesign
G.S.
New Building
CS
Constructing a new building
eo = 0.61
Assume Po + Dp2 = 1600 psf
DH =
0.1 x 16
1 + 0.61
1600
803
log
( )
=0.3 ft
Dr. Kamal Tawfiq - 2010
σ’o
D σ’ + σ’o
Consolidation Settlement
DH = log ( )
Cs H
1 + eO
D σ’ + σ’o
σ’o
D σ’
D σ’

## Slide 58
COEFFICIENT OF CONSOLIDATION (cv)
Generally decreases as Liquid Limit (LL) increases.
Determined from 1D Consolidation Test Lab per Load Increment.
Logarithm of Time Method
(Casagrande and Fadum, 1940)
Figure 7.19 Das FGE (2006).
Revised 03/2013
Slide 58 of 74
Square Root of Time Method
(Taylor, 1942)
Figure 7.20 Das FGE (2006).

## Slide 59
Revised 03/2013
Slide 59 of 74
Extend the straight line portion of primary and secondary consolidations to interest at Point A. Point A represents d100 (Deformation at 100% primary consolidation).
The initial curved portion of the deformation plot versus log t is approximated to be a parabola on a natural scale. Select times t1 and t2 on the curved portion such that t2 = 4t1. Let the difference of the specimen deformation between (t2 – t1) be equal to x.
Draw a line horizontal to DE such that the vertical distance BD is equal to x. The deformation corresponding to the line DE is d0 (Deformation at 0% primary consolidation).
COEFFICIENT OF CONSOLIDATION (cv)
Logarithm of Time Method

## Slide 60
50
Revised 03/2013
Slide 60 of 74
t50
0.197Hdr 2
H 2
cv =__________
T  0.197  cvt50
Logarithm of Time Method
4. The ordinate of Point F on the consolidation curve represents the deformation at 50% primary consolidation (d50).
5. For 50% average degree of consolidation (U = 50%), Tv = 0.197 (see Table 7.1, Das FGE 2006).
dr
or
Where:
Hdr = Average longest drain path during consolidation.
COEFFICIENT OF CONSOLIDATION (cv)

## Slide 61
Draw a line AB trough the early portion of the curve.
Draw a line AC such that OC = 1.15OB. The time value for Point D (i.e. the intersection of line AC and the data) is the square root of time for t90 (i.e. the time to 90% primary consolidation).
For 90% consolidation, Tv = 0.848 (see Table 7.1, Das FGE 2006).
90
Revised 03/2013
Slide 61 of 74
t90
0.848H 2
H 2
dr
cv = dr
T  0.848  cvt90
or
COEFFICIENT OF CONSOLIDATION (cv)
Square Root of Time Method

## Slide 62
(Bardet, 1997)

## Slide 63
Figure 7.26. Das FGE (2006).
Where:
Sp = Settlement due to structural load.
Sp+f = Settlement due to structural load and Fill.
Revised 03/2013
Slide 63 of 74
PRECOMPRESSION – GENERAL CONSIDERATIONS
Where:
Surcharge= p) +f)
p) = Change in vertical stress due to structural load.
f) = additional vertical stress due to Fill added.

## Slide 64: PRECOMPRESSION – PLANNING Mathematical Equations
14.330 SOIL MECHANICS Consolidation
Revised 03/2013
Slide 64 of 74
Definition of average Degree of Consolidation U
Substitution

## Slide 65: PRECOMPRESSION – PLANNING
14.330 SOIL MECHANICS Consolidation
Figure 7.27. Das FGE (2006).
Revised 03/2013
Slide 65 of 74
Where:
f) = Change in vertical stress due to Fill added.
p) = Change in vertical stress due to Structural Loading.
´o = Initial vertical effective stress.

## Slide 66: PRECOMPRESSION – PLANNING
14.330 SOIL MECHANICS Consolidation
STEPS:
Calculate primary consolidation settlement from planned loading (Sp).
Calculate primary consolidation settlement from planned loading plus surcharge (Sp+f ).
Calculate average degree of consolidation Note U = S(p)/S(p+f).
Find Tv from calculated U. To find time to when surcharge loading should be removed (i.e. t2):
dr
cv
Tv H 2
t2 

## Slide 67: GROUND MODIFICATION FOR CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
Figure 10.39. Das PGE (2006).
2
3
5
STEPS 1
Sand Drain Installation: Auger Method
(Kirmani, 2004)
Place auger at drain location.
Screw auger to selected depth.
Rotate auger at selected depth to remove soil.
Inject sand while auger is extracted.
Complete sand drain to working platform level.
SAND DRAINS

## Slide 68
Slide 74 of 74
Revised 03/2013
Settlement Platforms
Permanent Fill
Drainage Blanket
Piezometers
Soft Clay Vertical Drain
Firm Soil
Not to Scale
Inclinometers
SURCHARGING INSTRUMENTATION EXAMPLE
Surcharge
Courtesy of www.nhi.fhwa.dot.gov

## Slide 69: GROUND MODIFICATION FOR CONSOLIDATION PREFABRICATED VERTICAL DRAINS (PVD’S) (A.K.A. WICK DRAINS)
Slide 68 of 74
Revised 03/2013
14.330 SOIL MECHANICS Consolidation
Courtesy of www.nilex.com
Courtesy of www.nilex.com
Courtesy of www.americandrainagesystems.com

## Slide 70: GROUND MODIFICATION FOR CONSOLIDATION PREFABRICATED VERTICAL DRAINS (PVD’S) (A.K.A. WICK DRAINS)
14.330 SOIL MECHANICS Consolidation
Conceptual Concept
Courtesy of www.americanwick.com
Courtesy of www.americandrainagesystems.com
Figure 7.31. Das FGE (2006).

## Slide 71: GROUND MODIFICATION FOR CONSOLIDATION AVERAGE DEGREE OF CONSOLIDATION DUE TO VERTICAL & RADIAL DRAINAGE
14.330 SOIL MECHANICS Consolidation
Sand
Drain
Sand
Vertical and Radial Drainage
Courtesy of www.nhi.fhwa.dot.gov
Drainage
Clay
Uv,r  1  (1 Ur )(1 Uv )
Where:
Uv,r = Average Degree of Consolidation due to Vertical & Radial Drainage
Uv = Average Degree of Consolidation due to Vertical Drainage
Ur = Average Degree of Consolidation due to Radial Drainage

## Slide 72: GROUND MODIFICATION FOR CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
Section View
Figure 10.38. Das PGE (2006).
Plan View – Triangular Spacing
Figure 10.38. Das PGE (2006)
Reduction Drainage Path = Reduction in Drainage Time
SAND DRAINS
rw = Sand Drain Radius de = Effective Diameter

## Slide 73: GROUND MODIFICATION FOR CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
Plan View – Sand Drain Triangular Spacing Figure 7.30. Das FGE (2006).
w
o
vr
e
vr
r
w
r
r
kh
c t
m








e
c 
T 
n  de




 
m  






)
 (1  e
2r
ln(n) 
n 1
8T
U  1  exp
d 2
4n2
3n2 1
2
n2
Barron (1948)
de = Effective Diameter
rw = Sand Drain Radius
cvr = Coefficient of Radial Consolidation
Tr = Time Factor for Radial Consolidation
k = Coefficient of Horizontal Permeability
h
Tr = Time Factor for Radial Consolidation
eo = Initial Void Ratio
RADIAL CONSOLIDATION
Ur = Average Degree of Radial Consolidation

## Slide 74
TIME RATE OF RADIAL CONSOLIDATION
Variation of Tr with U - Table 7.3 Das PGE (2006).

## Slide 75
TIME RATE OF RADIAL CONSOLIDATION
Variation of Tr with U - Table 7.3 Das PGE (2006).

## Slide 82: SETTLEMENT FROM SECONDARY CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
C  e _____
log t2  log t1
Where:
C = Secondary Compression Index
e = Change in Void Ratio t = Time
Results of 1D Consolidation Test @ One Load Increment
Figure 7.15. Das FGE (2005).
Revised 03/2013
Slide 82 of 74

## Slide 83: SETTLEMENT FROM SECONDARY CONSOLIDATION
14.330 SOIL MECHANICS Consolidation
Where:
H = Height of Soil Layer
ep = Void Ratio @ End
of Primary Consolidation
t = Time
s
t
  
S  C H log
 1 
 t2 
C
1  ep
C 

Results of 1D Consolidation Test @ One Load Increment
Figure 7.15. Das FGE (2005).
Revised 03/2013

## Slide 84
Secondary Compression